ASSIGNMENT 2 – ROBOTICS

INTRODUCTION:

CHASSIS DESIGN:

METHODS:

evaluating the sensors and motors:

Before tackling the problems outlined in this assignment, it was first necessary to learn how the robot behaved during basic driving, sensing and actuating. Knowing how well the hardware performs is essential so that a plan for the robot can be built that does not incorporate the sources of error. We first measured for correlation between the robot's wheel encoders, the observed distance the robot travelled (in centimetres), and how long it took the robot to travel this distance.

As expected, time is constant whether we are dealing with an encoder value or a measured distance, and therefore the encoder values are also proportional to the speed of the robot. If we now arrange the graph so that the correlation between measured distance and encoder value is shown, the results are as so:
(A table displaying the numerical values can be found in the “Results” section)
Over a range of 14cm to 28cm the data displays a clear linear behaviour. To give a numerical value to this linearity of the data, we use the Pearson Correlation Coefficient (PCC) which values the correlation of a dataset from 1 (highly correlated) to 0 (not correlated) to -1 (inversely correlated):

(INSERT ALGORITHM HERE)

Dataset	Standard Deviation	Covariance	Pearson Cor. Coef.
Measured Distance	4.4458	407.65	0.99882
Encoder Distance	91.802

With a PCC of 1.0, it shows the measured distance and the encoder and perfectly linearly correlated. Measuring the slope of this line will therefore represent the correlation constant (to make the robot drive a given distance, use this value in the encoders). The slope is: (550.167 – 319)/(26.27-15.33) = 20.385 encoder/cm (note the average value of the trials is used).

For the development of an accurate dead-reckoning system, it is also essential to measure how the error of the robots ability to turn to a specific angle relative to the motor power and time. The same process used for measuring actual distance versus encoder distance was used to evaluate the angle and motor power. Below are the two graphs representing the behaviour:

For the second graph, power was kept constant and only the angle to time correlation was measured. The four distinct lines correspond to 15%, 25%, 35%, and 45%. For determining a time/angle constant, 25% power was chosen as a constant (as it was high enough to drive the robot without lag, but did not drive too fast such that sensors would lose measurement accuracy). The analysis of the linearity using PCC is below:

Dataset	Standard Deviation	Covariance	Pearson Cor. Coef.
Time	0.59761	32.929	0.86646
Angle	63.592

A PCC of 0.87 implies linear correlation between the time turned at 25% power and the angle of the robot. The slope of this dataset is therefore the time to angle constant: (120-27)/(2-0.5) = 62 degrees/second.

A dead-reckoning controller can now be designed using the above constants. The performance of the controller and its estimated errors are outlined below:

(TODO)

Target Angle (degrees)	Target Distance (cm)	Actual Angle (degrees)	Actual Distance (cm)	Error	Avg. Error of System

(TODO: sensor analysis)

Following the evaluation of the robot's behaviour, it is clear that the robot is accurate when driven within the testing environment, and therefore can be relied on to perform specific angle turns and driving tasks during this assignment.

following a line and the PID controller:

Developing an algorithm that was generic and adaptable to a multitude of scenarios was essential to the line following task. The classic line following technique involves driving the robot's left wheel forward when the colour detected is white/black and driving the robot's right wheel forward when the colour is the opposite. This is a naive approach that does not make use of the fact that when the robot is perfectly aligned, both wheels can be driven (and oscillation removed). Below is an example of the Naive Line Following Algorithm:

http://www.societyofrobots.com/member_tutorials/book/export/html/350

The less-naive approach is to devise a gradient, such that the further a robot is from the line, the sharper it will turn toward the line. For the sake of argument, we assume white colour has a value of 0 (sensor units) and black has a value of 100 (sensor units). As the light sensor value approaches 0, the error should approach a maximum value of 1 (TODO: use limit alg. representation) and as the light sensor value approaches 100, the error should approach the minimum value of -1. This method is shown below:

When there is no error (the robot is exactly on the boundary of on and off the line), the robot should drive straight; an error of 1 should increase the value of the power of the robot's left wheel and decrease the power of the robot's right wheel, and visa versa for an error of -1. The final step to complete the gradient line-following algorithm is to assign the robot a constant value for the wheel power, c, and a constant value to multiply the error by and power the turning. This entire process is no more than a P (Proportional) Controller system, where the constant for the error is kp in the algorithm such that: d = kp (t – l), where t = the light value of 50 (in the above graph) and t = the current light value.

To determine a value for kp, a constant wheel power, c, was set to 25% (something low so that it is easy to analyse) and a range of values were assigned to kp. Below are graphs of the robot's position over time, showing how much or how little the robot oscillated:

kp = 10
 kp = 15

kp = 20
kp = 30
kp = 40

(TODO: determine where to put this part) The line following algorithm required a colour sensor value for both black light and white light. The naive approach to this is pre-determine the black and white colour values and and hand code these as constants. The problem with this approach is that changes in the environment's lighting, the height of the sensor, and other factors can cause the colour sensor values to change dramatically. To make the robot adaptable to a variety of line-following scenarios, the robot begins the line-following algorithm by completing a full 360 degree rotation using the gyroscope sensor and recording the range of light values it sees during this rotation. A histogram is then created using the light values. The largest maximum that is the lowest light value is selected as the black colour constant and the largest maximum that is the highest light value is selected as the white constant. The 'target' value for the line-following algorithm is the average of these two values. A plot of an example histogram is shown below:

(IMAGE OF LIGHT SENSOR HISTOGRAM)

robot states:

handling broken lines:

avoiding obstacles:

The algorithm for avoiding obstacles was similar to the line following algorithm, but used the ultrasonic sensor to calculate and adjust the distance from the obstacle.

RESULTS:

DISCUSSION: